## Slide 1: Risk Matrix
Hazard Identification &
Unit A: Fitting and Machining
Lesson 2.3

## Slide 2: LESSON OVERVIEW
ACTIVITIES
Spot the Hazards (Image-Based)
Case Study Walkthrough
Worksheet: Hazard ID & Risk Matrix
Today, you will learn how to:
Spot hazards in a workshop environment
Assess risks using a 3x3 Risk Matrix
Apply control measures using the Hierarchy of Controls
Think like a safety-conscious professional to prevent accidents before they happen
RESOURCES
Workshop Hazard Images
Risk Matrix Template (3x3)
Hierarchy of Controls Visual Pyramid
HAZARD ID & RISK MATRIX
Notes: QCAA Links: 4.3.1, 4.3.4, 3.1.1
"Today we're learning to think critically about dangers in the workshop - not just what could go wrong, but how to judge the level of risk and choose the right response."

## Slide 3: Why Workshop Safety Skills Matter
Hazards are everywhere in a workshop – knowing how to spot them, assess the risk, and take action could prevent serious harm. These skills will serve you well in any profession in a practical setting.
HAZARD ID & RISK MATRIX
Notes: Hand Files / Engineers Files – 3
https://technologystudent.com/equip1/hfile3.htm
How to File Metal: 12 Steps (with Pictures) – wikiHow
17 Different Types of File Tools & Uses in Workshop [PDF]

## Slide 4: Key Definitions
Hazard vs risk
Hazard: Something with the potential to cause harm
Risk: The chance (likelihood x consequence) of that harm actually occurring
Frayed electrical cord
Electric shock if touched
Hazard
Risk
vs
Can anyone give a real-world example?
HAZARD ID & RISK MATRIX
Notes: Hand Files / Engineers Files – 3
https://technologystudent.com/equip1/hfile3.htm
How to File Metal: 12 Steps (with Pictures) – wikiHow
17 Different Types of File Tools & Uses in Workshop [PDF]

## Slide 5: Common Workshop Hazards
Rotating machinery - risk of entanglement or crush injuries
Sharp tools and edges - cuts, lacerations, or punctures
Electrical hazards - damaged cords, exposed wires, faulty outlets
Flammable materials – fire from swarf, oily rags, or chemicals
Cluttered floors - slips, trips, and blocked exits
Chemical exposure – skin or respiratory harm from coolant, lubricants, cleaning agents
Missing or damaged safety signage – unclear procedures or unnoticed hazards
Machines left unattended while in use – accidental activation/misuse
Incorrect tools used for tasks – poor results, tool breakage, or injury
Working alone – delayed emergency response or unnoticed incidents
Poor PPE use – no eye, hand, or hearing protection ↑ severity of injury
HAZARD ID & RISK MATRIX
Notes: "These are the kinds of hazards you might see every day in a fitting and machining workshop. Let’s get familiar with what to look out for - because spotting them is the first step in staying safe."

## Slide 6: Key Hazard Map Zones
Zone | Hazard | Signs
Lathe/Mill Area | Rotating parts, flying debris | Eye protection, entanglement warning
Grinding Station | Sparks, noise, dust | Eye protection, hearing and respiratory PPE
Bench Work Area | Sharp tools, repetitive strain | Cut hazard, ergonomic
Chemical Storage | Coolants, flammable liquids | Flammable + toxic symbols
Floor / Walkways | Slips, trips, clutter | Slip hazard, floor marking
Tool Storage | Falling tools, poor access | Secure storage symbol
Electrical Panels | Shock, exposed wiring | Electrical danger icon
HAZARD ID & RISK MATRIX
Notes: "These are the kinds of hazards you might see every day in a fitting and machining workshop. Let’s get familiar with what to look out for - because spotting them is the first step in staying safe."

## Slide 7: Spot the Hazards
Identify the hazards.
What risks might they pose?
HAZARD ID & RISK MATRIX
Notes: Hand Files / Engineers Files – 3
https://technologystudent.com/equip1/hfile3.htm
How to File Metal: 12 Steps (with Pictures) – wikiHow
17 Different Types of File Tools & Uses in Workshop [PDF]

## Slide 8: What is a Risk Matrix?
It is a visual tool used to assess and prioritise risks by evaluating two key factors:
  Likelihood: How probable it is that a hazard or incident will occur
  Consequence: The severity of the impact if the incident does occur
The two dimensions are plotted on a grid – commonly 3x3, 4x4, or 5x5 – where each cell represents a level of risk (e.g. low, medium, high).
  X-axis: Consequence (Minor - Major)
  Y-axis: Likelihood (Unlikely – Likely)
  Labels: Low, Medium, High
The intersection of likelihood and consequence helps determine the risk rating, which guides decisions about control measures.
It is useful in engineering and workshop settings to:
  Justify safety controls
  Prioritise hazards
  Communicate risk clearly to students and staff
HAZARD ID & RISK MATRIX
Notes: Hand Files / Engineers Files – 3
https://technologystudent.com/equip1/hfile3.htm
How to File Metal: 12 Steps (with Pictures) – wikiHow
17 Different Types of File Tools & Uses in Workshop [PDF]

## Slide 9: Control Measures & Hierarchy of Controls
Control Measures are actions or strategies used to eliminate or reduce risk
Use the Hierarchy of Controls – a system that ranks safety strategies from most to least effective
Level | Description | Example
Elimination | Remove the hazard completely | Use a safer process instead of a lathe
Substitution | Replace the hazard with something safer | Use plastic instead of metal
Engineering Controls | Isolate people from the hazard | Guarding, fume extraction
Administrative Controls | Change the way people work | Training, procedures, supervision
PPE (Least Effective) | Protect the individual | Safety glasses, gloves, hearing protection
Not all controls are equal – PPE is important, but it’s our last line of defense.
Always work from the top down.
HAZARD ID & RISK MATRIX
Notes: Hand Files / Engineers Files – 3
https://technologystudent.com/equip1/hfile3.htm
How to File Metal: 12 Steps (with Pictures) – wikiHow
17 Different Types of File Tools & Uses in Workshop [PDF]

## Slide 10: Reassess the Risk (Post-Control)
After control measures, reassess the hazard using the same matrix
This is called the residual risk
Ask:
  Has the likelihood gone down?
  Have we reduced the consequences?
If the risk is still high → More controls needed!
Risk management isn’t a checklist – it’s a cycle.
HAZARD ID & RISK MATRIX
Notes: Hand Files / Engineers Files – 3
https://technologystudent.com/equip1/hfile3.htm
How to File Metal: 12 Steps (with Pictures) – wikiHow
17 Different Types of File Tools & Uses in Workshop [PDF]

## Slide 11: Scenario Walkthrough – Applying the Matrix
Case: Swarf Build-Up Near Lathe
What’s the hazard?
  Swarf accumulation – Loose metal shavings (swarf) piling up under or around the lathe work area
What’s the risks?
  Cuts from sharp swarf
  Slips or trips if debris isn’t cleared
  Entanglement with rotating parts
  Fire risk from flammable or reactive metal chips
  Machine faults (jamming) due to swarf buildup
HAZARD ID & RISK MATRIX
Notes: Hand Files / Engineers Files – 3
https://technologystudent.com/equip1/hfile3.htm
How to File Metal: 12 Steps (with Pictures) – wikiHow
17 Different Types of File Tools & Uses in Workshop [PDF]

## Slide 12: Scenario Walkthrough – Applying the Matrix
Case: Swarf Build-Up Near Lathe
Rate the likelihood and consequence
  Likelihood: Possible – Swarf frequently builds up during turning
  Consequence: Moderate – Slips, cuts, machine jamming
HAZARD ID & RISK MATRIX
Notes: Hand Files / Engineers Files – 3
https://technologystudent.com/equip1/hfile3.htm
How to File Metal: 12 Steps (with Pictures) – wikiHow
17 Different Types of File Tools & Uses in Workshop [PDF]

## Slide 13: Scenario Walkthrough – Applying the Matrix
Case: Swarf Build-Up Near Lathe
Rate the likelihood and consequence
  Likelihood: Possible – Swarf frequently builds up during turning
  Consequence: Moderate – Slips, cuts, machine jamming
  Risk Level: Medium
HAZARD ID & RISK MATRIX
Notes: Hand Files / Engineers Files – 3
https://technologystudent.com/equip1/hfile3.htm
How to File Metal: 12 Steps (with Pictures) – wikiHow
17 Different Types of File Tools & Uses in Workshop [PDF]

## Slide 14: Scenario Walkthrough – Applying the Matrix
Case: Swarf Build-Up Near Lathe
Control Measures (Hierarchy – go from top down):
  Elimination: Not practical – swarf is unavoidable byproduct
  Engineering Control: Install swarf trays or chip guards
  Administrative Control:
    Enforce regular clean-up schedules
    Include swarf disposal steps in relevant SOPs
    Reminder signage in lathe areas
    Provide training
  PPE: Ensure use of gloves and safety glasses
What control measure is best here?
Why isn’t PPE the first option?
HAZARD ID & RISK MATRIX
Notes: Hand Files / Engineers Files – 3
https://technologystudent.com/equip1/hfile3.htm
How to File Metal: 12 Steps (with Pictures) – wikiHow
17 Different Types of File Tools & Uses in Workshop [PDF]

## Slide 15: Scenario Walkthrough – Applying the Matrix
Case: Swarf Build-Up Near Lathe
Reassess with control measures in place:
  Likelihood: Possible – Swarf still builds up during turning
  Consequence: Minor – with swarf trays, PPE, training, signage
  Risk Level: Low
HAZARD ID & RISK MATRIX
Notes: Hand Files / Engineers Files – 3
https://technologystudent.com/equip1/hfile3.htm
How to File Metal: 12 Steps (with Pictures) – wikiHow
17 Different Types of File Tools & Uses in Workshop [PDF]

## Slide 16: Activity: Spot the Hazards
Refer to Hazard ID & Risk Matrix Worksheet
(work in pairs: 30min)
HAZARD ID & RISK MATRIX
Notes: Hand Files / Engineers Files – 3
https://technologystudent.com/equip1/hfile3.htm
How to File Metal: 12 Steps (with Pictures) – wikiHow
17 Different Types of File Tools & Uses in Workshop [PDF]

## Slide 17: Share Findings
Class share-out:
What hazards did you identify?
What was the final risk ratings?
What control measures did you choose?
Did anyone’s group find a high-risk situation? How did you lower it?
HAZARD ID & RISK MATRIX
Notes: Hand Files / Engineers Files – 3
https://technologystudent.com/equip1/hfile3.htm
How to File Metal: 12 Steps (with Pictures) – wikiHow
17 Different Types of File Tools & Uses in Workshop [PDF]

## Slide 18: What We Covered
A hazard is something with the potential to cause harm
A risk is the chance that harm will occur from a hazard
We explored common workshop hazards and key danger zones
We learned how to use a 3x3 Risk Matrix to assess risks
We applied the Hierarchy of Controls to reduce risk effectively
We practiced assessing and managing hazards through real-world scenarios.
HAZARD ID & RISK MATRIX
Notes: Hand Files / Engineers Files – 3
https://technologystudent.com/equip1/hfile3.htm
How to File Metal: 12 Steps (with Pictures) – wikiHow
17 Different Types of File Tools & Uses in Workshop [PDF]

## Slide 19: WHS Reminder
Always think before you work – identify hazards before interacting with tools or materials
Use tools responsibly – Understand the risk, then choose the safest approach
Report unsafe situations – Spot it, speak it, stop harm
Next lesson: Tool Identification – because knowing your equipment is the next step in risk control
Safety isn’t a slide, it’s a habit.
Spot the hazard. Think through the risk. Act with control.
HAZARD ID & RISK MATRIX
Notes: Hand Files / Engineers Files – 3
https://technologystudent.com/equip1/hfile3.htm
How to File Metal: 12 Steps (with Pictures) – wikiHow
17 Different Types of File Tools & Uses in Workshop [PDF]