## Slide 1: Tool Identification & Safety
Unit A: Fitting and Machining
Lesson 2.4

## Slide 2: LESSON OVERVIEW
ACTIVITIES
Station Rotations (x3):
Measuring & Marking
Cutting & Holding
Threading & Fastening
Tool ID & Safety Worksheet
What You’ll Learn
Identify key tools by name, type, category, and function
Know the differences between hand tools, power tools, and machinery (equipment) and when to use them
Recognise safe practices and PPE for each tool group
Understand the basic workshop processes: Measure → Mark → Hold → Cut → Tap → Fasten
RESOURCES
Tools & Station Setup
Tool ID & Safety Worksheet
Information Sheets: Tool Summary & Machinery Equipment
Glossary of Workshop Terms
TOOL ID & SAFETY
Notes: QCAA Links: 4.3.1, 4.3.4, 3.1.1
"Today we're learning to think critically about dangers in the workshop - not just what could go wrong, but how to judge the level of risk and choose the right response."

## Slide 3: Types of Tools
TOOL ID & SAFETY
Category | Hand Tools | Power Tools | Machinery (Equipment)
Definition | Manually operated tools for basic tasks | Electrically or pneumatically powered handheld tools | Stationary powered equipment for precision machining
Power Source | Manual (human effort) | Electric, battery, or compressed air | Electric or hydraulic (stationary)
Portability | Portable | Portable | Non-portable (fixed in place)
Operation | Fully manual | Mechanised (hand-guided) | Automated or semi-automated
Speed | Slow – depends on user effort | Fast – significantly reduces task time | Very fast – designed for high-volume precision
Examples | File, hacksaw, taps and tap handle | Cordless drill, angle grinder | Drill press, lathe, milling machine, bandsaw
Use Case | Small and simple tasks | Speed, moderate tasks | Heavy-duty, precision machining
Skill Level | Basic | Intermediate | Advanced (requires training)
Safety Risk | Low – minor cuts, repetitive strain | Moderate – flying debris, kickback, noise | High – entanglement, crushing, rotating parts
Cost | Low – affordable, minimal maintenance | Moderate – higher upfront, some maintenance | High – expensive, requires upkeep and training
Power Tools
Machinery (Equipment)
Hand Tools
Notes: Hand Files / Engineers Files – 3
https://technologystudent.com/equip1/hfile3.htm
How to File Metal: 12 Steps (with Pictures) – wikiHow
17 Different Types of File Tools & Uses in Workshop [PDF]

## Slide 4: Choosing the Right Tool for the Task
TOOL ID & SAFETY
Tool Type | When to Use | Why It’s Chosen
Hand Tools | Precision marking, filing, tapping Small adjustments or finishing touches | Low cost High control Ideal for beginners (basic skills)
Power Tools | Drilling holes Grinding edges Shaping | Faster than hand tools Good for repetitive tasks Moderate skill level
Machinery (Equipment) | Machining parts High precision drilling Demonstration of lathe use | High accuracy Industrial relevance Requires training and supervision
Power Tools
Machinery (Equipment)
Hand Tools
Link to Industry Practice
  Metal Fabrication: Precision parts shaped using drill presses, grinders, lathes, milling machines, and tapping tools
  Engineering Workshops: Safe, efficient production through hand skills and machine use (e.g. drill presses, lathes, grinders, bandsaws, tapping tools)
  Manufacturing Industry: High-volume output achieved with automated tools – highlighting accuracy and consistency
Notes: Hand Files / Engineers Files – 3
https://technologystudent.com/equip1/hfile3.htm
How to File Metal: 12 Steps (with Pictures) – wikiHow
17 Different Types of File Tools & Uses in Workshop [PDF]

## Slide 5: Tool Categories By Function
Measuring (e.g. Steel rule, Vernier Caliper, Protractor)
Marking (e.g. Scriber, Centre punch)
Holding (e.g. Bench Vice, G-Clamp)
Cutting (e.g. Hacksaw, Files, Drill, Saw, Angle Grinder)
Threading (e.g. Tap & Die Sets)
Fastening (e.g. Bolts & Nuts, Drill)
🪚
✏️
TOOL ID & SAFETY
📏
🔩
Notes: Hand Files / Engineers Files – 3
https://technologystudent.com/equip1/hfile3.htm
How to File Metal: 12 Steps (with Pictures) – wikiHow
17 Different Types of File Tools & Uses in Workshop [PDF]

## Slide 6: Measuring Tools
Function: Used to determine dimensions like length, width, height, depth, or angles.
Hand Tool Examples: steel rule, vernier calipers, protractor, vernier height gauge, combination square
Safety Tips:
  Double-check measurement before cutting or drilling to prevent mistakes.
  Store sharp-edged tools like calipers properly to avoid cuts.
TOOL ID & SAFETY
Steel Rule
Caliper
Vernier Height Gauge
Protractor
Combination Square
Notes: "These are the kinds of hazards you might see every day in a fitting and machining workshop. Let’s get familiar with what to look out for - because spotting them is the first step in staying safe."

## Slide 7: Marking Tools
Function: Help transfer measurements to a material by marking lines or reference points.
Hand Tool Examples: Scriber, center punches, divider, number/letter punch set, ball pein hammer
Safety Tips:
  Be cautious with sharp tools like scribers – they can cause cuts.
  Use a rule or straight edge as a guide to avoid slipping when marking.
  Mark clearly but gently to avoid damaging delicate materials.
  Clean surfaces and avoid oily surfaces before marking
TOOL ID & SAFETY
Scriber
Centre Punch
Divider
Number / Letter Punch Set
Permanent Marker Pen
Engineer’s Blue
Ball Pein Hammer
Notes: "These are the kinds of hazards you might see every day in a fitting and machining workshop. Let’s get familiar with what to look out for - because spotting them is the first step in staying safe."

## Slide 8: Holding Tools
Function: Holding tools are used to grip secure or stabilise a workpiece while you work on it.
Hand Tool Examples: Vices, clamps, V block, soft jaws
Safety Tips:
  Use the right size tool for the job to avoid slippage
  Check for wear or damage – worn teeth or loose grips can cause accidents
  Keep fingers clear of moving or clamping parts
  Tighten clamps securely, but don’t overdo it – you don’t want to damage the material
TOOL ID & SAFETY
Bench Vice
G-Clamp
F-Clamp
V Block
Soft Jaws
Notes: "These are the kinds of hazards you might see every day in a fitting and machining workshop. Let’s get familiar with what to look out for - because spotting them is the first step in staying safe."

## Slide 9: Cutting Tools
Function: Used to remove material – either by slicing, shearing, grinding or shaping.
Hand Tool Examples: Hacksaws, files
Power Tool Examples: Cordless drill, angle grinder, metal cut-off saw
Safety Tips:
  Always cut away from the body
  Wear gloves to protect your hands from sharp edges. Do not wear gloves when using rotating tools – they can get caught and cause injury.
  Use safety glasses to shield your eyes from flying debris or sparks.
  Keep blades sharp – dull tools require more force and can slip
  Secure your workpiece so it doesn’t move while cutting
  Clean up metal or wood shavings to avoid slips or cuts
TOOL ID & SAFETY
Hacksaw
Flat File
Half-Round File
Cordless Drill
Angle Grinder
Metal Cut-Off Saw
Notes: "These are the kinds of hazards you might see every day in a fitting and machining workshop. Let’s get familiar with what to look out for - because spotting them is the first step in staying safe."

## Slide 10: Threading Tools
Function: Create screw threads – either internal (with taps) or external (with dies)
  Taps cut threads inside a hole so a bolt or screw can go in.
  Dies cuts threads on the outside of rods or bolts.
Hand Tool Examples: Tap & tap handles, die & die stock, thread gauge, tap guide block
Power Tool Example: Cordless drill (with tapping attachment)
Safety Tips:
  Wear gloves to protect hands from sharp threads and edges. Do not wear gloves when using rotating tools – they can get caught and cause injury.
  Use eye protection – metal shavings can fly during cutting.
  Apply cutting oil to reduce friction and prevent tool damage.
  Turn slowly and back off regularly to avoid snapping the tap / die.
  Use correct tap/die size for the material and hole/rod.
  Secure workpiece before threading.
TOOL ID & SAFETY
Taps
Tap Handles
Die & Die Stock
Thread Gauge
Tap Guide Block
Tapping Compound / Cutting Paste
Tapping
Compound
Drill with Tapping Attachment
Notes: "These are the kinds of hazards you might see every day in a fitting and machining workshop. Let’s get familiar with what to look out for - because spotting them is the first step in staying safe."

## Slide 11: Fastening Tools
Function: Hold parts together securely using threaded connections.
  Bolts & screws join materials.
  Nuts secure bolts.
  Washers spread the load and prevent damage.
Hand Tool Examples: Spanners, screwdrivers, allen keys
Power Tool Example: Cordless drill (with screwdriver tip)
Safety Tips:
  Use properly sized tools (e.g. spanners, screwdrivers) to avoid slipping.
  Avoid overtightening – it can strip threads or snap bolts.
  Watch your hands and knuckles when tightening in tight spaces.
  Keep fasteners organised to avoid mix-ups or sharp points in toolboxes.
TOOL ID & SAFETY
Washers
Bolts
Spanners
Nuts
Screws
Screwdrivers
Allen Keys
Drill with Screwdriver Tip

## Slide 12: Safety & PPE
TOOL ID & SAFETY
Task | PPE Needed | Why It’s Important
Measuring & Marking | Safety glasses Lightweight gloves (optional) | Protects eyes from stray dust, metal chips, or sharp scribers
Cutting & Holding | Safety glasses Cut-resistant gloves (only for handling, not while operating rotating tools) Covered footwear | Guards hands from blades and splinters, eyes from flying debris
Threading & Fastening | Safety glasses Nitrile or mechanic gloves (only for handling, not while operating rotating tools) | Prevents injury from sharp threads and oils.
Always tuck in loose clothing and tie long hair back before tools.
🪚
✏️
🔩
📏

## Slide 13: Demo & Station Overview
Teacher Demo → Station Rotations
Teacher will demo tools for Stations 1 & 2 beforehand. Station 3 demo will happen at the station.
Station 1: Measuring & Marking (10 mins)
  Tools: steel rule, divider, combination square, marking ink, scriber, ball pein hammer, number/letter punch set
  Task: Measure and mark out an item template
Station 2: Threading & Fastening (10 mins)
  Tools: Tap + tap handle, tapping compound, bolts, cordless drill
  Task: Tapping and fastening technique
Station 3: Cutting & Holding (20 mins)
  Tools: Hacksaw, flat file, bench vice, G-clamp, cordless drill, angle grinder, metal cut-off saw
  Task: Cut and file samples
TOOL ID & SAFETY
Fill out your Tool ID & Safety worksheet as you rotate through the stations.
Notes: Tips:
Use power tools as demo-only or teacher-guided stations unless students have completed formal induction and risk assessments.
Rotate students through stations with clear roles; observer, handler, and recorder.
Reinforce industry practices by comparing hand vs power tools efficiency, accuracy, and safety
Link tasks to artefact production (e.g. drill gauge holes, mallet handle shaping)