## Slide 1: Technical Drawing
Module 3.1
Orthographic and Pictorial Views

## Slide 2: Technical Drawing
Topics
What is technical drawing?
What is pictorial drawing?
What is orthogonal projection?
ISO projections
Module 3.1

## Slide 3: Learning Objectives
By the end of this module, students will be able to :
Recognise what is technical drawing
Recognise types of pictorial drawing
Recognise ISO projections
LEARNING OBJECTIVES

## Slide 4: Technical Drawings
What is technical drawing?
What is technical drawing?
Technical drawing, also known as drafting is a precise and unambiguous visual representation of how something is constructed or functions. Unlike artistic drawings, which are subjective and expressive, technical drawings focus on accurately and clarity.
Technical drawing is descriptive and require a set of rules, term, and symbols that its readers can understand and use. A technical drawing of a part may be drawn in NSW, the part could be made in QLD and sent to the WA for assembly. To successfully accomplished this process, there should be one standard interpretation of technical drawings.
Most countries set up a standards committees to accomplish this. In Australia, technical drawing standard is established by Standards Australia and the standards is AS 1100.101 Technical drawing, Part 101: General principles.
Artist impression
A section of technical drawing
Notes: Extra resources:
Branoff, T. J., Jensen, C. H., Hines, R., & ProQuest. (2016). Interpreting engineering drawings (Eighth edition.). Cengage Learning.
Everything You Need To Know About Technical Drawings , https://draftings.com.au/everything-you-need-to-know-about-technical-drawings/
What Is Technical Drawing? – Darnell Technical Services Inc. , https://darnelltechnical.com/what-is-technical-drawing/
AS 1100.101 Technical drawing, Part 101: General principles.
AS 1000 The international System of Units (SI) and its applications.
AS1100.201 Technical drawing, Part 201: Mechanical drawing.

## Slide 5: Technical Drawings
Why are they important?
Why are they important?
Artist impression
A section of technical drawing
Technical drawings are important because of the following:
Communication: It convey design details like dimensions and materials.
Accuracy: Ensure exact dimensions and tolerances are displayed.
Record keeping: Served as a record of how the parts was constructed for future maintenance or replacement.
Safety: identify critical information such as material and load bearing capacity.
Cost efficiency: Help identify and reduce error, saving time and cost.
Notes: Extra resources:
Branoff, T. J., Jensen, C. H., Hines, R., & ProQuest. (2016). Interpreting engineering drawings (Eighth edition.). Cengage Learning.
Everything You Need To Know About Technical Drawings , https://draftings.com.au/everything-you-need-to-know-about-technical-drawings/
What Is Technical Drawing? – Darnell Technical Services Inc. , https://darnelltechnical.com/what-is-technical-drawing/
AS 1100.101 Technical drawing, Part 101: General principles.
AS 1000 The international System of Units (SI) and its applications.
AS1100.201 Technical drawing, Part 201: Mechanical drawing.

## Slide 6: Technical Drawings
Producing engineering drawings
Due to the requirement of accuracy and short turnaround time from product design to manufacturing, many industries have shifted to using CAD (Computer Aided Design) software to create design in 3D or 2D models, and precise technical drawings. There are several CAD software, which are widely used across different industry such as: SolidWorks, Fusion 360, SketchUp and AutoCAD.
This Unit does not cover the utilisation of CAD software but students should understand that technical drawings are usually generated using CAD software.
Producing engineering drawings
Notes: Extra resources:
Manual drafting: see Parthasarathy, N. S., & Murali, V. (2015). Engineering drawing. Oxford University Press.

## Slide 7: Technical Drawings
Pictorial Drawing
A pictorial drawing is a type of technical drawing that shows an object as it appears to the eye, giving a more realistic view of its shape and structure. Unlike orthographic drawings (which show multiple 2D views like front, top, and side), pictorial drawings represent the object in 3D on a 2D surface, making it easier to visualize.
There are three main types of pictorial drawings:
Isometric Drawing
Oblique Drawing
Perspective Drawing
1) Isometric [1]
2) Oblique [1]
3) Perspective [1]
Pictorial Drawing
Notes: Notes:
Isometric Drawing
-Shows the object with the axes at 120° angles.
-All dimensions are to scale, but the angles are distorted.
-Common in engineering and technical design.
Oblique Drawing
-The front face is drawn true to scale and shape.
-The depth is represented at an angle (usually 45°), often not to scale.
-Common in marketing brochure to explain the product features.
Perspective Drawing
-Mimics how the human eye sees objects.
-Uses vanishing points to create depth.
-Often used for artistic or architectural purposes.
Reference:
1. Branoff, Ted. Interpreting Engineering Drawings, Cengage, 2015. ProQuest Ebook Central, page 2. https://ebookcentral.proquest.com/lib/qut/detail.action?docID=6798671.

## Slide 8: Technical Drawings
Orthogonal Projection
Orthogonal projection is a method of representing 3D objects in 2D, where the projection lines are perpendicular to the projection plane. Since the project lines are at 90° to the drawing plane, it produces true shape and sizes of each view. Multiple orthogonal projections (multiple views) are commonly used in a technical drawing to show the shape and dimensions of the part.
Since several views of a part are normally required to describe a shape, the view position must be clearly identified in the drawing.
Parallel projection [1]
Orthogonal Projection
Notes: Reference:
1. Giesecke, Frederick, et al. Technical Drawing with Engineering Graphics, Pearson Education, Limited, 2023. page 51. ProQuest Ebook Central, https://ebookcentral.proquest.com/lib/qut/detail.action?docID=7216926.

## Slide 9: Technical Drawings
ISO Projections
There are two methods of the orthogonal projection, namely third angle projection and first angle projection. The differences between the two are as follow:
Third angle projection: Each view is placed so that it represents the side of the object near to it in the adjacent view.
First angle projection: Each view is placed so that it represents the object remote from it in the adjacent view.
In Australia, the third angle method of projection is preferred. Since there are two types of projections, the AS 1100.101 required all drawings to indicate the method of projection in the title block. The International Organization for Standardization (ISO) projection symbols are as below:
Third angle projection [1]
First angle projection [2]
ISO Projection Symbol
Notes: Reference:
Branoff, Ted. Interpreting Engineering Drawings, Cengage, 2015. Page 25. ProQuest Ebook Central, https://ebookcentral.proquest.com/lib/qut/detail.action?docID=6798671.
Branoff, Ted. Interpreting Engineering Drawings, Cengage, 2015. Page 26. ProQuest Ebook Central, https://ebookcentral.proquest.com/lib/qut/detail.action?docID=6798671.