## Slide 1: Dimensions, Scales and Symbols
Module 3.2

## Slide 2: Dimensions, Scales, and Symbols
Topics
What is dimensioning?
What do those dimension symbols represent?
Project requirements
Module 3.2

## Slide 3: Learning Objectives
By the end of this module, students will be able to :
Recognise project requirements
Interpret drawing symbols
Recognise annotations and scales
LEARNING OBJECTIVES

## Slide 4: Activity
Could you make this accurately?
What's missing?
Introduction to Dimensioning

## Slide 5: Technical Drawings
Introduction to Dimensioning
Dimensions are shown on drawing by dimension line, leaders, arrowheads, notes, and symbols. These define the geometrical characteristic of the angles, diameters and distance.
Projection and dimension lines [1]
Introduction to Dimensioning
Notes: Notes:
Image taken from AS1100.101. Those dimension lines marked * present the ISO recommended practice, but it may be desirable for clarity to omit the line between projection lines as shown by that marked ƚ . The detail information of the leaders, arrowheads and line sizes are provided in AS 1100.101.
Reference:
1. AS 1100.101 Technical drawing, Part 101: General principles.

## Slide 6: Technical Drawings
Dimensioning Symbols
Dimensioning symbols are used in technical drawing to improve. Clarity, accuracy and efficiency.
Definition and application of dimension symbols from AS 1100.101
Dimensioning Symbols
Notes: Notes:
The table above shows the common dimensioning symbols used in technical drawings. Standard dimensioning symbols in technical drawings are crucial for clarity, accuracy, and efficiency.
1. Standardization –ensuring universal understanding across different engineers, manufacturers, and designers.
2. Precision – They eliminate ambiguity, making sure measurements are interpreted exactly as intended.
3. Efficiency – Using symbols instead of text saves space, making the drawing clearer and easier to read.
4. Consistency – They ensure uniformity across different drawings, reducing the chance of misinterpretation.
Reference:
1. AS 1100.101 Technical drawing, Part 101: General principles.

## Slide 7: Technical Drawings
Title Block
Title block usually embedded in the drawing located in the bottom right-hand corner of the drawing sheet.
Typical title block for A1, A2, and A3 size sheets [1]
Legend:
Name of the design authority.
Drawing title.
Drawing number.
Record of information relative to preparation of the drawing.
Code identification number also known as revision number.
Drawing sheet size designation.
Predominant scale of the drawing.
Reserved for miscellaneous information i.e. mass or number of multiple sheets drawing.
J. Additional block as required for general information i.e. dimensioning and tolerancing notes, finish, drawn and approval names or material.
Title Block
Notes: Notes:
A typical title block shall consist the following information:
Name of the organisation, department.
Title of the drawing.
Drawing number.
Signatures or initial and dates.
The scale, method of projection.
Sheet size.
Other relevant information.
Refer AS 1100:101 for more information on drawing sheet sizes and layout.
Reference:
1. AS 1100.101 Technical drawing, Part 101: General principles.

## Slide 8: Technical Drawings
Project Requirements and Drawing Details
Dimensioning symbols are used in technical drawing to improve. Clarity, accuracy and efficiency.
Project Requirements and Drawing Details
Notes: Notes:
The drawing above is an example of a technical drawing. It contains information about the part's form, size (scale), and surface finish details. Here are information from the drawing:
Notes consolidate the information regarding the engineer's or designer's design intent.
This is an annotation for the fabricator/installer, indicating that special attention is required.
When objects are drawn to their actual size, it is called full scale or scale 1:1. However, large objects such as ships or turbines are too big to be drawn in full scale, so they must be represented at a reduced scale. In this drawing, the part is shown at an enlarged scale of 2:1 to highlight its features. Dimensions should not be scaled.
Show the hole callout. Top example: A thru hole with a diameter of 3.4mm with counterbore diameter of 6.6mm and 2.4mm depth.
Show the form and size of the part.
The finish condition of the part’s surfaces shall be completed using 600-grit wet and dry sandpaper.
Specifies the material and grade that should be used for fabrication.
Reference:

## Slide 9: Technical Drawings
Project Requirements
Technical drawings play a crucial role in identifying potential hazards and applying control measures in various industries, particularly engineering, manufacturing, and construction.
Here are how technical drawings can contribute to identify and apply control measures to potential hazards:
Hazard identification:
Sharp edges and corners,
Incorrect tolerances,
Material considerations,
Assembly and clearance issues,
Electrical or thermal hazards.
Control measure implementation
Use annotation and notes
Standardised symbols,
Regulatory compliance,
Assembly Instructions
Project Requirements
Notes: Notes:
Hazard Identification
Sharp Edges and Corners: Detailed dimensioning allows engineers to spot potential sharp edges that might cause injury, prompting design adjustments (e.g., chamfering or rounding edges).
Incorrect Tolerances: Poorly specified tolerances can lead to misfits or weak joints, increasing failure risks.
Material Considerations: Technical drawings specify materials and their grade, ensuring appropriate selection to prevent mechanical failure or corrosion.
Assembly and Clearance Issues: Overlapping or misaligned parts may create pinch points or stress points, leading to hazardous conditions.
Electrical or Thermal Hazards: Drawings indicate heat dissipation areas, insulation requirements, or electrical component placement, preventing overheating or electrical risks.
Control Measures Implementation
Use Annotations & Notes: Drawings include explicit instructions on handling specific risks (e.g., "Do not chamfer cutting face" or "Ensure proper grounding").
Standardized Symbols: Using AS/ ISO symbols for drawing symbols ensures universal understanding.
Regulatory Compliance: Conforming to industry standards (ISO, OSHA, AS/NZS) ensures compliance with local regulations.
Assembly Instructions: Explains step-by-step installation and maintenance procedures, reducing human errors and accidents.