## Slide 1: Hole Sizes & Tolerances
Module 3.3

## Slide 2: Hole Sizes and Tolerances
Topics
What does a standard drawing include?
Holes information and location
Tolerances and limits
Surface roughness
Module 3.3

## Slide 3: Learning Objectives
By the end of this module, students will be able to :
Examine standard technical drawing
Recognise hose sizes and limits
Recognise surface roughness rating
Interpret tolerances
LEARNING OBJECTIVES

## Slide 4: Technical Drawings
Standard Drawing
View of the object of different sides.
Dimension with tolerances.
P.C.D – Pitch hole diameter.
Indicate the holes information and location.
Callout for different holes sizes and dimensions.
Surface finish requirement. This symbol indicate that the surface is to be machined to a specific requirement, which is Ra=0.8 m.
Standard Drawing
Notes: Note:
The default surface finish on other surfaces ais Ra=1.6.

## Slide 5: Technical Drawings
Surface Roughness Comparison
Ra is the area roughness between a roughness profile and the mean line.
Notes: Note:
The image on the right side is a surface roughness comparator based on different machine techniques. The table on the left is an indication of surface roughness on various applications.
Resource:
A Comprehensive Guide to Surface Roughness, its Measurement, Standards, and Charts (https://www.kemalmfg.com/cnc-machining/surface-roughness/)
Surface Roughness Chart Guide: Symbols, Values & Measurement (https://www.rapiddirect.com/blog/surface-roughness-chart/)

## Slide 6: Technical Drawings
Dimension Limits and Tolerances
Tolerance of linear dimension [1]
Dimension Limits and Tolerances
Notes: Notes:
Bore hole size shall not more then 20.50mm or less then 20.25mm. The shaft is shall not larger than 20.20mm or smaller than 20.18mm.
20.25 <= Hole diameter <= 20.50
Liner tolerance between 34.75-35.25mm
Reference:
1. AS 1100.101 Technical drawing, Part 101: General principles.

## Slide 7: Technical Drawings
Types of Engineering Fits
Clearance fit – bearings, linkages and sliding parts, gears, plumbing fittings.
Transition fit – gear and pulley systems, bearing assemblies, automotive wheel hubs.
Interference fit – Tool fixtures, precise assemblies
Clearance fit[1]
Transition fit[1]
Interference fit[1]
Types of Engineering Fits
Notes: Notes:
1. Clearance Fit
Definition: A clearance fit occurs when there is always a gap between the hole and the shaft, allowing for free movement.
Characteristics:
  The shaft is always smaller than the hole.
  Allows easy assembly and disassembly.
  Used where relative motion is required between parts.
2. Transition Fit
Definition: A transition fit can result in either a small clearance or a small interference, depending on the actual sizes of the hole and shaft.
Characteristics:
  Offers a compromise between clearance and interference fits.
  Used where accurate location is important but some freedom of movement is acceptable.
  May require light force for assembly.
3. Interference Fit
Definition: An interference fit occurs when the shaft is always larger than the hole, requiring force or heat for assembly.
Characteristics:
  Creates a very tight joint.
  No relative motion between parts after assembly.
  Often used for permanent or semi-permanent assemblies.
Extra resources:
Types of Engineering Fits: Clearance, Interference & Transition Explained – Alibre , https://www.alibre.com/blog/types-of-engineering-fits-clearance-interference-transition-explained/
Types of Fit in Engineering: Clearance, Transition, and Interference , https://www.fictiv.com/articles/engineering-fits-clearance-transition-interference

## Slide 8: Interpret Tolerances
Can you identify the tolerance upper and lower limits?
Interpret Tolerances
Notes: Reference:
1. AS 1100.101 Technical drawing, Part 101: General principles.

## Slide 9: Interpret Tolerances
Answer
Interpret Tolerances
Notes: Reference:
1. AS 1100.101 Technical drawing, Part 101: General principles.