## Slide 1: Sections & Material Naming Conventions
Module 3.4

## Slide 2: Sections & Material Naming Conventions
Topics
Common polymers
Steel sections
Module 3.4
ACTIVITIES
Worksheet 3.4

## Slide 3: Learning Objectives
By the end of this module, students will be able to :
Recognise the naming convention of various polymers
Identify steel sections acronyms
LEARNING OBJECTIVES

## Slide 4: Technical Drawings
 | Chemical name | Description
ABS | Acrylonitrile Butadiene Styrene | A Terpolymer made by polymerizing styrene and acrylonitrile. It is widely used in appliance housings, luggage, pipe fittings, and automotive interior parts.
Acetal/ POM | Polyoxymethylene | Engineering thermoplastic used in precision parts requiring high stiffness, low friction, and excellent dimensional stability.
Acrylic/ PMMA | Polymethyl methacrylate | A transparent thermoplastic.
Nylon/ PA | Polyamide | A silk-type appearance that can be form into diverse shapes.
PC | Polycarbonate | High impact resistance thermoplastic.
PEEK | Polyether ether ketone | Semicrystalline thermoplastic with excellent mechanical and chemical resistance properties that are retained to high temperatures
PET | Polyethylene terephthalate | Most common thermoplastic polymer resin used in clothing fibre, container for liquids and foods.
PVC | Polyvinyl chloride | A synthetic plastic polymer available in a rigid or flexible form.
Polymers
Common polymers
Polymers
Notes: Notes:
The material properties of each polymers can be found in the resources.
Resources:
Tynic | Engineering Plastics Selection Guide (https://tynic.com.au/engineering-plastics-selection-guide/)
Machinable Plastics Guide: How to Make the Right Choice (https://www.china-machining.com/blog/best-machinable-plastics/)
Most common machinable plastics – AGCIS (https://agcis.com/machinable-plastics/)

## Slide 5: Technical Drawings
Section Type | Description | Common Uses
Flat Bar | Rectangular cross-section, flat and solid | Framing, brackets, supports
Round Bar | Solid cylindrical profile | Shafts, pins, decorative elements
Square Bar | Solid square profile | General fabrication, supports
Equal Angle (EA) /Unequal Angle (UA) | L-shaped profile, available in equal or unequal leg lengths | Structural framing, corner protection, brackets
Parallel Flanged Channel (PFC) | C-shaped profile with two flanges and a web | Framing, tracks, enclosures
Tee (T-Section) | T-shaped profile | Structural applications, joining sections
Square hollow section (SHS) | Square hollow profile | structural application, frame, supports
Rectangular hollow section (RHS) | Rectangular hollow profile | structural application, frame, supports
Tube/ Circular Hollow Section (CHS) | Round hollow section | Piping, frames, furniture, automotive parts
Universal Beam (UB) | Also known as I-beam, name after the letter “I” | Structural applications, framing
Universal Column (UC) | Also know as H beam, the width and height are also equal. | Structural applications, framing
Mild Steel and Aluminium sections
Sections are pre-formed using extrusion method. The versatile shapes can be used for a variety of applications. Standards cover these sections is AS/NZS 2679: Structural steel hot-rolled bars and sections.
Standard Sections
Notes: Notes:
The standard dimensions of each sections can be found in the resources link below.
Resources:
Aluminium Angles and Geometric Extrusions | Capral Aluminium, https://www.capral.com.au/extrusion-plate-sheet/extrusion/angles-geometrics/
AS/NZS 3679: Structural Steel - Hot-Rolled Bars and Sections
Structural Steel - Southern Steel WA, https://www.southernsteelwa.com.au/structural-steel/

## Slide 6: Technical Drawings
Mild Steel and Aluminium sections
Standard Sections
Notes: Notes:
The standard dimensions of each sections can be found in the resources link below.
Resources:
Aluminium Angles and Geometric Extrusions | Capral Aluminium, https://www.capral.com.au/extrusion-plate-sheet/extrusion/angles-geometrics/
AS/NZS 3679: Structural Steel - Hot-Rolled Bars and Sections
Structural Steel - Southern Steel WA, https://www.southernsteelwa.com.au/structural-steel/
References:
Structural Steel, https://www.southernsteel.com.au/structural-steel/
Structural Tube & Pipe , https://www.southernsteel.com.au/structural-tube-pipe/
Tee Section, T Beam, T Bar - Handy Steel Stocks , https://handysteel.com.au/miscellaneous-tee-section#product