## Slide 1: How To Use A Bandsaw
Module 4.1

## Slide 2: Learning Objectives
LEARNING OBJECTIVES
By the end of this module, students will be able to:
Identify what a vertical and horizontal bandsaw is
Select correct WHS and PPE for the bandsaw
Identifying parts of a bandsaw
Use the tooling and fixtures for the bandsaw and how they work
Demonstrate correct and safe operation of the bandsaw
Understand some troubleshooting and maintenance

## Slide 3: What is a bandsaw?
A stationary machine used to cut material to length
Provides better accuracy, control, repeatability and safer mounting
Commonly used in metalworking, woodworking, and fabrication
Definition of a Bandsaw
What are its uses?
Cutting of material to achieve a desired length
Repeatability using stops
Variable speed for cutting different materials
Type of bandsaws
Horizontal
Vertical
Can lend themselves to cutting smaller parts and easy to manipulate part manually
Cut straight
Can swivel to cut angles
Vise for arcuate clamping

## Slide 4: Machinery safety & Personal protective equipment
Why Safety Matters?
Exposed and High-Speed Blade
  Cuts and amputations from contact with the blade.
  Kick back from dull, worn (missing blade teeth) or blade weld joins
  Potential entanglement from loose clothing or jewelry
Material Hazards
  If a work piece isn’t clamped securely, it can spin or fly out of control, hitting anyone in the vicinity
  Bandsaws generate airborne dust and debris, risk to respiratory and eye hazards
Tool related injuries
  Using the wrong blade or incorrect speed can cause excessive heat, smoke or flying debris
  Installing blades can cause cuts – Use gloves for installing, not running.
Sharp edges and Hot surfaces
  Bands are extremely sharp
  Material can heat due to friction of cutting – If possible, use coolant
PPE
  Safety glasses/face shield, safety boots, Hearing protection (if necessary), No loose clothing-gloves-jewelry, tie back long hair.
SAFETY & PPE

## Slide 5: Cleanliness
Ensuring a safe and clean workspace for you and your classmates
Effective Housekeeping
  Make sure the work area is in a clean and tidy state before you start work and when you finish work to minimize the risk of slips trips and falls
Safety
  Make sure to use correct PPE when cleaning (don’t handle the swarf with bare hands)
  Don’t use compressed air on the machines, it can send sharp swarf through the air and or get it caught in the working/moving parts of the machine
  Make sure guards are in place and work as recommend by manufacturer
SAFETY CULTURE

## Slide 6: BANDSAW COMPONENTS
BANDSAW COMPONENTS
Safety features;
  E-STOP
  Safety Guard
Driving features;
  Blade Tensioner
  Motor speed select
  Start Switch
  Feed adjustment
  Blade
  Coolant
Mounting and fixture features;
  Vise
  Height Limit Stops
  Material Length Stops
ESTOP
Safety Guard
Blade Tensioner
Vise Adjustment
Motor Speed Adjustor
Controls
Vise
Blade

## Slide 7: Cutting speeds calculations
IDENTIFIERS
Bandsaws will come with specified speeds in the owner’s manual, or an information plate maybe attached to the machine.
Blade lengths are important as they will need to be replaced. These are commonly identified on a plate attached to the Bandsaw. The 330mm on this plate identifies the widest cut possible of round stock

## Slide 8: How to operate a Horizontal Bandsaw
OPERATION
https://www.youtube.com/watch?v=rSqC3i8jjrU
Notes: Key Moments
Anatomy of the Bandsaw – 0:21
Fluid Flow Valve – 1:00
Saw Feed Rate Knob – 1:16
Blade Guide Supports – 1:31
Roller Conveyor Stands – 2:30
Cutting Work Aid – 2:55
PPE – 3:17
Set the Blasé Guide Support – 5:33
Adjust the Blade Fluid Valve – 6:02
Make a Cut at an Angle – 6:47

## Slide 9: Deburring the material
DEBURRING
It is always important to Deburr edges of material after cutting. Edges can be extremely sharp.
There are many tools used for deburring material, including files and handheld tools shown below.

## Slide 10: Cleaning up after yourself
Cleaning up after yourself in the workshop is very important, it helps prevent the chances of slips trips and falls as a build up of swarf and coolant can become slippery underfoot.
Cleaning down the machine once you have finished helps prolong the life of the machinery and makes it easier for the next student to start work. Applying a small amount of oil or oil-based spray to the bare metal parts of the machine can prevent surface rust and make clean up after use easier.