## Slide 1: How To Use A Drill Press
Module 4.3

## Slide 2: Learning Objectives
LEARNING OBJECTIVES
By the end of this module, students will be able to:
Identify what a drill press is
Select correct WHS and PPE for the drill press
Identifying parts of a drill press
Use the tooling and fixtures for the drill press and how they work
Demonstrate correct and safe operation of the drill press
Understand some troubleshooting and maintenance

## Slide 3: What is a drill press??
A stationary machine used to drill precise holes
Provides accuracy, control, repeatability and safer mounting
Commonly used in metalworking, woodworking, and fabrication
Definition of a drill press
What are its uses??
Drilling holes with exact depth and control
Reaming, countersinking and tapping holes (depending on the model)
Drilling through harder materials safely
Other names may also be; Pedestal drill and Bench drill
Notes: https://www.safeworkaustralia.gov.au/sites/default/files/2023-08/whs-principles-factsheets_overview_august2023.pdf - Factsheet
https://www.qld.gov.au/education/schools/procedures/health
https://www.safework.nsw.gov.au/__data/assets/pdf_file/0006/586347/guide-to-machine-safety.pdf
https://www.australianworkplacesafety.com.au/safe-use-of-machinery-and-equipment-in-australian-workplaces/
https://education.qld.gov.au/curriculum/stages-of-schooling/CARA/activity-guidelines/practical-workshop-activities

## Slide 4: Machinery safety & Personal protective equipment
Why Safety Matters?
High speed rotating parts
  The spinning drill bit and chuck can catch clothing, gloves, hair and jewelry
  Fingers can be severely injured or amputated if they come in contact with the rotating bit
Material Hazards
  If a work piece isn’t clamped securely, it can spin or fly out of control, hitting anyone in the vicinity
  Drilling into hard or unknown material can cause the bit to break or jam
Tool related injuries
  Using the wrong bit or incorrect speed can cause excessive heat, smoke or flying debris
  A loose chuck key left in the chuck can shoot out like a bullet when the machine is started
Sharp edges and Hot surfaces
  Drill bits and freshly drilled holes can become extremely hot and cause burns
  Swarf (metal shavings) are sharp and dangerous. NEVER remove it by hand
PPE
  Safety glasses/face shield, safety boots, Hearing protection (if necessary), No loose clothing-gloves-jewelry, tie back long hair.
SAFETY & PPE

## Slide 5: Cleanliness
Ensuring a safe and clean workspace for you and your class mates
Effective Housekeeping
  Make sure the work area is in a clean and tidy state before you start work and when you finish work to minimize the risk of slips trips and falls
Safety
  Make sure to use correct PPE when cleaning (don’t handle the swarf with bare hands)
  Don’t use compressed air on the machines and it can send sharp swarf through the air and or get it caught in the working/moving parts of the machine
SAFETY CULTURE

## Slide 6: Different types of “Drill press’s”
DRILL PRESS STYLES
Gear driven, Drill Press
Belt driven, Drill Press
Single belt drive
Double belt drive

## Slide 7: DRILL PRESS COMPONENTS
DRILL PRESS COMPONENTS
Safety features;
  E-STOP
  Safety Guard
Driving features;
  Gear Change Handles
  Motor speed select
  Start Switch
  Quill (feed) Handle
Mounting and fixture features;
  Table and clamping system
  Table height adjuster and lock
  Chuck

## Slide 8: Fixtures for the slotted table
Table fixtures
Engineers vice
T-Slot Quick Clamps
T-Slot Clamping Kit

## Slide 9: Tooling and tooling mounting
CUTTING TOOLS
HSS twist drills
Step drill bit, Cone/conical drill bit,
Christmas tree drill bit
HSS reamer
Countersinking Drill bit
Morse taper
quick change hex drive

## Slide 10: Twist drills cutting angles/faces
CUTTING ANGELS
It is important to get the Lip Length even across both sides for the drill bit to correctly on both edges
The most common cutting angle for a drill bit that cuts multi material is 118
If I Drill is incorrectly Sharpened it can lead to excessive heat, cutting over/under size, squealing, jamming, chatter and breaking/shattering the drill bit

## Slide 11: Tool mounting options
Jacobs chuck
TOOL MOUNTING
Keyed chuck
Key less chuck
Morse Tapper
The Jacobs chuck is a tool holding system that will hold objects with a straight shank
When you tighten the chuck by twisting the head by hand or with the key, three teeth will eject from the body tightening on the object that is inside the chuck
The Morse Tapper is a Precision ground tapper that matches a standard so they can be used across multiple machines and adapters so mountings can be cross compatible
The Morse Taper works by friction, when slid in the the suiting female side the surface area of the Precision ground faces lock them selves together

## Slide 12: Drilling cycles and coolants
DRILLING AND COOLING
Pecking dill cycle
Coolant
Repeat steps until you have drilled through the material
Coolant
Machining coolant, also known as cutting fluid, is a liquid used in machining operations to cool the cutting tool and work piece, lubricate the cutting area, and flush away chips and debris. It plays a vital role in preventing damage to the machine and work piece, increasing tool life, and improving surface finish.

## Slide 13: HSS twist drill cutting speeds calculations
SPINDLE SPEEDS
“Simplified formula”
RPM = (Cutting Speed (m/min) * 320) / Drill Diameter (mm)
Cutting Speeds m/min;
  Stainless steel = 12
  Tools Steel = 18
  Cast Iron = 24
  Malleable iron = 27
  Medium carbon steel = 30
  Free cutting steel = 43
  Aluminium/Brass = 61
  Wood/Plastic = 91
Medium carbon steel
10mm drill diameter
“example”
RPM = 12 * 320 = 3,840 ÷ 5 = 768 RPM
Stainless steel
5mm drill diameter
“class exercise”
RPM? = Aluminium * 320 = ? ÷ 8mm drill bit = ? RPM
“example”
RPM = 30 * 320 = 9,600 ÷ 10 = 960 RPM

## Slide 14: How to operate a drill press
OPERATION
Notes: Introduction (5 min)
Facilitator provides context: why consent is important in ensuring student safety and compliance.
Discuss common challenges in obtaining and managing consent.
Brainstorming (10mins) – identify pain points in processes (delays, missing forms, tracking issues etc)
Tools & strategies:
Digital platforms for electronic consent collection (Google Forms, Microsoft Forms etc),
Using centralised tracking system (Excel sheets, school database integration),
Automating reminder systems to ensure timely responses,
Standardising consent forms to make them clear, consider and easy to access,
Involving school administration for bulk processing and support,
Parent engagement strategies to enhance communication and response rates.
During Group Discussion & Refinement (10mins)
Group share their insights and ideas with larger group
Facilitator guides a discussion on feasibility, implementation challenges, and school-specific considerations
Identify best practices that can be implemented collectively

## Slide 15: Deburring the material
DEBURRING
It is always important to Deburr the holes after they have been drilled to remove any sharp edges to eliminate the chances of cuts or improper fitments.
There are many tools used for deburring material, including the chamfering bits and these hand held tools shown below. If none are available you can always use a file.

## Slide 16: Cleaning up after yourself
Cleaning up after yourself in the workshop is very important, it helps prevent the chances of slips trips and falls as a build up of swarf can become slippery underfoot.
Cleaning down the machine once you have finished helps prolong the life of the machinery and makes it easier for the next student to start work. Applying a small amount of oil or oil based spray to the bare metal parts of the machine can prevent surface rust and make clean up after use easier.