## Slide 1
Module 5.10
Basic Operations Of A Manual Milling Machine & Tooling

## Slide 2: Learning Objectives
LEARNING OBJECTIVES
By the end of this module, students will be able to:
Identify what a manual milling machine is and what it is used for .
Select safety features of a milling machine and how to work safely around a mill.
Identify main parts and accessories on a milling machine.
Safe mounting procedures of materials.
Identify tooling used on a milling machine.
Evaluate speeds and feeds for machining on a mill.
Understand how to operate safely and basic understanding of machining procedures
Proper clean up and pack up of machine after use

## Slide 3: What is a manual milling machine, and why would you use it?
MILL EXPLANATION
A manual milling machine is a machine tool used to shape and cut metal or other solid materials using a rotating cutting tool. Unlike CNC milling machines, which are controlled by computer programs, manual milling machines are operated by hand using wheels, dials, and levers to move the work piece and cutting tool. There are three main types of manual milling machine;
  Vertical Milling Machine
  Horizontal Milling Machine
  Universal Milling Machine
They are commonly used in workshops for tasks such as one-off parts, small production runs, re-machining/claiming parts and simple modifications. They are more affordable and easier to maintain, making them a practical choice for general-purpose machining.
Notes: https://www.safeworkaustralia.gov.au/sites/default/files/2023-08/whs-principles-factsheets_overview_august2023.pdf - Factsheet
https://www.qld.gov.au/education/schools/procedures/health
https://www.safework.nsw.gov.au/__data/assets/pdf_file/0006/586347/guide-to-machine-safety.pdf
https://www.australianworkplacesafety.com.au/safe-use-of-machinery-and-equipment-in-australian-workplaces/
https://education.qld.gov.au/curriculum/stages-of-schooling/CARA/activity-guidelines/practical-workshop-activities

## Slide 4: Different types of milling machines
MILL TYPES
Vertical Milling Machine
Horizontal Milling Machine
Universal Milling Machine

## Slide 5: Safety features on a manual milling machine
MILL SAFETY
As the vertical milling machine is the most common milling machine found out in industry that is the one we will be focusing on. Some of the safety features found on this machine are;
  E-stop button
  Proper Lighting and Work Area Markings
  Torque sensors
  Manual set hard stops for the saddle side control
  Table and Saddle Locks
  Electrical Interlocks

## Slide 6: PPE while operating the milling machine
MILL SAFETY
PPE (personal protective equipment) is the first thing you should think of before operating the manual mill. There are many risks and hazards while operating the machine including;
Flying debris, rotating objects, moving parts, pinch points, sharp objects/surfaces and hot surfaces.
Here is a list of the PPE required to be wearing while operating the manual mill;
  Safety glasses
  Hard Toe safety shoes
  Hearing protection (if required)
  No loose fitting clothes or long sleeves
  Tie up long hair
  No jewellery
  No Gloves while the machine is being operated (Only while cleaning)

## Slide 7: Safe working area around a mill
MILL SAFETY
Making sure the working area around and on the mill is in a clean, tidy and safe state, this is important to reduce any hazards while operating the machine. If there is left over swarf (metal shavings), coolant or oils left on the mill it can create a hazard while operating the machine for cutting your hands or having your hand slip when turning the handles.
The surrounding area should also be clear of objects or obstacles that can impede your movement around the machine or any exits that you may need to move towards quickly.

## Slide 8: Identifying the main parts of a manual mill
IDENTIFYING PARTS
.
Motor; This drives the milling machine Spindle
Head (drive); This controls the Speed of the spindle spinning
Quill feed handle; Drives the quill up and down(can have automatic feeding)
Quill; A hollow tube that holds the spindle and can independently move up and down
Spindle; Holds and rotates the cutting tool and is driven by the motor
Swivel (turret); Holds the upper part of the mill and able to rotate moving the head in two positions required for some setups
Worktable; T-slotted table that the work piece is mounted to or other mounting options
Saddle; Holds the worktable and moves it in the X and Y axis
Cross traverse Hand wheel; Hand wheels that turn the lead screws driving the table in the X and Y axis
Knee; Base that holds the saddle and worktable and can be driven up and down in the Z axis
Column; The upright that determines the height of the milling machine
Base; Where the machine will be mounted to the ground and normally has a chip pan to catch the swarf (metal shavings)

## Slide 9: Material mounting options
WORK PIECE MOUNTING
There are a few options for mounting the work piece on to the worktable for machining;
Vice – Secures the work piece to the machine table.
Clamping Kits – Hold larger or irregular-shaped work pieces using T-slots
Chucks – Secures the work piece to the machine table.
Rotary Tables – Allow circular machining and precise angle cuts.
Dividing Heads – Used for gear cutting or spacing holes and slots evenly.
Parallels and Angle Plates – Assist in accurate work positioning

## Slide 10: Milling machine working axes
“CLOCKING”
Milling machines move on three axes;
  X axis; traveling left to right on the machine
  Y axis; traveling towards and away from you
  Z axis; traveling up and down
A handy tip while trying to remember which way they move is to use this right hand rule shown in the top right corner

## Slide 11: Squaring up and “clocking”
“CLOCKING”
When mounting fixtures and material to the work table you have to “clock” them in, meaning making the clamping faces or the part to be machined run parallel with the Z and x axis. This can be done with the help of a dial indicator. This is important to get as close to “zero(0)” as possible to make sure your job is correctly machined or your slots/hole alignments won’t be parallel with the edges of the work piece.

## Slide 12: Squaring up and “clocking”
“CLOCKING”
The best and easiest way to “clock” up the vice is by mounting a dial indicator to the base of the spindle with a magnetic base (making sure not to turn the machine on). Apply the tip of the dial indicator to the fixed jaw of the chuck and traverse the work table side to side in the X axis while adjust the vice by tapping it around until the dial indicator doesn’t move and reads “0” for the length of the jaw. Do the same in the Z axis to make sure everything is square and parallel with the travel of the mill
Dial indicator
Magnetic base

## Slide 13: Setting material in a vice with parallels
MATERIAL CLAMPING
If you want to clamp the material in the vice and It is too short to reach the bottom of the vice you can use parallels. Parallels are precision ground bars of steel that can hold up your material so the cutter clears the jaws of the chuck.
TIP; It helps to tap down the material when it’s in the vice with a dead blow hammer to make sure it is fully contacting the base of the vice

## Slide 14: Tooling used on a milling machine
MILL TOOLING
There are many types of tooling for a milling machine, these are the more common ones;
End Mills
  Used for cutting slots, profiles, and contours.
  Comes in 2-flute - 4-flute
Slot Drills
  Centre-cutting tools used for plunging and slotting.
Face Mills
  Used to machine flat surfaces quickly with multiple cutting edges.
Fly Cutters
  Single-point cutting tool for large surface finishes.
Drill Bits
  For drilling holes; typically used with a drill chuck in the spindle.
Reamers
  For finishing drilled holes to a precise size with a smooth finish.
Spot-drill
  Used for aligning drills, making grooves and chamfering.

## Slide 15: Tooling Direction
MILL TOOLING
Milling cutters spin in a clockwise direction turning the cutting faces in to the material to be cut. There are two main types of milling processes, climb milling and conventional milling. It is recommended to do conventional milling on a manual milling machine where a CNC machine will normally cut in a climb milling direction.
Conventional milling
Climb milling

## Slide 16: Tooling holders
MILL TOOLING HOLDERS
Collet chucks & collets (ER or R8)
  Precision holders for end mills and drills.
Drill Chuck (Jacobs chuck)
  Holds standard twist drills.
Milling Arbor
  Used for holding large diameter cutters like slitting saws
Shell Mill Hold
  For holding face mills or other larger cutters.

## Slide 17: Speeds and feeds for machining on a milling machine
SPEEDS AND FEEDS
Speeds and feeds are essential settings used in milling to control how fast the cutting tool moves and how much material it removes. Setting them correctly helps improve tool life, surface finish, and safety. The tooling RPM is the same formula as the drilling. You can only see the cutting feed rate if your milling machine has automatic feeding. The formula for for feed rates on the milling machine is:
Example;
Feed Rate=RPM * Number of Teeth * Feed per Tooth,
Feed per Tooth depends on the material and tool size, often ranging from 0.02 to 0.2 mm/tooth
Number of Teeth is the number of cutting edges on the milling tool.

## Slide 18: Speeds and feeds for machining on a milling machine
SPEEDS AND FEEDS
Medium Carbon Steel | 20 – 30 m/min | Use coolant to extend tool life
Cast Iron | 10 – 20 m/min | No coolant required; can be run dry
Stainless Steel | 15 – 25 m/min | Tough material; use coolant
Aluminium and Alloys | 80 – 200 m/min | Can be cut at high speeds; use lubricant
Brass | 80 – 120 m/min | Cuts easily; avoid too much coolant
Plastics (Acrylic, Nylon) | 100 – 300 m/min | Use high speeds, low feed; watch heat build-ups

## Slide 19: Spindle speed exercises!!
SPEEDS AND FEEDS
You're milling aluminium with a 10 mm end mill:
Cutting Speed: 150 m/min
Tool Diameter: 10 mm
Number of Teeth: 2
Feed per Tooth: 0.1 mm
RPM = (300 × 150) ÷ 10 ≈ 4500 RPM Feed Rate = 4500 × 2 × 0.1 = 900 mm/min
Meters per Minute
Notes: Work through as a class

## Slide 20: Setting the spindle RPM on the Milling machine
SPINDLE SPEEDS
Setting the spindle speed on the milling machine is done while the mill is running.
DO NOT ADJUST THE SPINDLE SPEED WITH THE SPINDLE RUNNING
There is normally a handle on the head of the milling machine that can be rotated and a dial on the front will turn over reading the speed the spindle is running at. The milling machine can also be run in high gearing and low gearing (note normally in the low gearing the spindle will spin in reverse so you need to run the machine in reverse to counteract)
Speed handle
Speed indicator

## Slide 21: Tooling feed rates
FEEDS
For mills with auto feeding there is a small dial you can turn on the auto feed controllers to increase or decrease the feed rate of the tooling

## Slide 22: Manual mill operation
MANOEUVRING THE MILL
X axis travel
(move side to slide)
Z axis travel
(move the knee)
Moving the working table on a manual milling machine is done by winding hand wheels in a clockwise and anti clockwise direction, the two handles on either end of the working table move the X axis from side to side, both handles work independently. The handle on the front of the knee moves the Y axis in and out. The bigger handle down the bottom of the knee drives the Z axis by lifting and lowering the knee. You have to push in the handles to engage them into the driving mechanism.
The quill can also be lowered by the handle on the head to help drilling or line boring. Its good practise to lock the quill before you start the milling process.
Y axis travel
(move in and out)
Moving the quill

## Slide 23: Starting the spindle on the mill
STARTING THE MILL
To start the mill you turn the ON switch located on the mill. It will say forward and reverse, remembering to run the milling machine in reverse when cutting in low gear. Make sure you watch which way the cutter is rotating and that it is spinning clockwise.
Switch to start the machine

## Slide 24: Locating the work piece on the manual mill
WORK LOCATION
There are a few ways of locating the material on the milling machine. There are tools you can put in the chucks or collets called edge finders which wiggle then run true (straight) when they have found the edge of the material. Or you can bring your cutter in to contact with the material until it just takes a cut then you can “ZERO” out the D.R.O or the analogue gauge on the hand wheels on the mill (just like the manual lathe).
Edge finder

## Slide 25: Finding your “Z-0”
“Z-0” is the zero point of your z height where you start taking your depths of cuts from. The easiest way to find your “Z-0” is to bring the milling cutter in to contact with the highest point of your material that will be machined. Then zero out the D.R.O or the analogue gauge on the hand wheels. Then begin the machine process, remembering to move the cutter into a clear space on the milling bed and test the feed rates if the mill has the capability.
DATUM POINTS “Z-0”

## Slide 26: Cleaning and packing up the machine
CLEANING
Once you have finished using the manual Mill you should clean it, as this is the best and safe practice. Make sure the machine is completely turned off before you start the cleaning process. If you are handling sharp objects make sure you wear gloves. Use a vacuum, pliers (if the swarf is stuck) and rags to clean down the Mill. Once it is clean use some oil or oil based spray to clean and wipe down the bed ways for longevity of the machine. Always return the cutters to where they came from don’t leave them in the machine.

## Slide 27: resources
Photos;
https://www.goldenmachinery.com/blogs/5-main-parts-of-a-lathe-machine
https://en.wikipedia.org/wiki/Lathe
https://newsigns.com.au/products/no-gloves-in-toilet-sign
http://www.homews.co.uk/page548.html
https://www.istockphoto.com/search/2/image-film?phrase=people%20doing%20math%20equations
https://www.machineryhouse.com.au/l639d