## Slide 1: Tap Thread to Specifications
Module 5.16

## Slide 2: PROJECT OVERVIEW
Topics
Hole tapping tools
Different Types of Taps
Types of Tapping Threads
MODULE 5.16

## Slide 3: Learning Objectives
By the end of this module, students will be able to:
Able to select appropriate tools for hole tapping operations.
Perform simple hole tapping.
LEARNING OBJECTIVES

## Slide 4
Meat Mallet
Thread tapping is the process of cutting internal threads in a hole so that a fastener (like a bolt or screw) can be inserted.
Tools needed for thread tapping:
Taper tap
Intermediate tap
Bottoming tap
Tap handle (aka T-tap wrench)
Engineering square
Lubricant
Thread Tapping

## Slide 5: Different Types of Taps
There are several types of taps, each design for specific tasks.
1. Taper Tap
  Features: Long chamfer (7–10 threads), gradual cutting.
  Use: Starting threads in a hole; easiest to align.
  Best for: Through holes or deep blind holes.
2. Intermediate Tap
  Features: Medium chamfer (3–5 threads).
  Use: General-purpose threading.
  Best for: After using a taper tap.
3. Bottoming Tap
  Features: Short chamfer (1–2 threads).
  Use: Cutting threads to the bottom of a blind hole.
  Best for: Finishing threads started by taper tap.
Meat Mallet
Taper tap
Intermediate tap
Bottoming tap

## Slide 6: Types of Tapping Threads
There are many different types of threads, each design for specific applications in mechanical, plumbing, or electrical. The common tapping thread are:
Metric Thread (M – coarse thread / fine thread)
  Standard in most of the world
  Designated by diameter and pitch (e.g., M16 × 2)
Unified Thread (UNC/UNF)
  Common in the U.S.
  UNC: Coarse thread
  UNF: Fine thread
National Pipe Tapered (NPT)
  Taper thread
  Common for sealing
Meat Mallet
British Standard Whitworth (BSW)
  Coarse thread with a 55° thread profile
  Used in older British machinery
British Standard Fine (BSF)
  Fine thread with a 55° thread profile
British Standard Brass (BSB)
  Parallel thread
  Commonly use with brass
Notes: Resource:
Common type of tapping threads : https://www.paengineeringsupplies.com.au/tapping-drilling-chart/

## Slide 7: External Thread Cutting Tools
Tools you need for external thread cutting are:
Cutting die
Wrench
Lubricant
Engineering square
Meat Mallet