## Slide 1: Correct Tooling Selection For Lathe Operations
Module 5.5

## Slide 2: Learning Objectives
LEARNING OBJECTIVES
By the end of this module, students will be able to:
Identify different types of lathe tooling and what they are made from.
Identify the tooling used in various turning applications.
Develop an understating of how the cutting faces/angles work.
Develop an understating of how to set the tooling in the holders and on centre.

## Slide 3: What is Lathe tooling?
LATHE TOOLING
Metal lathe tooling, refers to the various tools and attachments used with a metal lathe to cut, drill, thread, finish and shape/form metal work pieces. Tooling is essential for performing different operations accurately and efficiently.
Metal lathe tooling, can be made from multiple different tool materials. Each tool is chosen based on the job requirements — such as the type of metal being machined, the cutting speed, and the desired finish.
Notes: https://www.safeworkaustralia.gov.au/sites/default/files/2023-08/whs-principles-factsheets_overview_august2023.pdf - Factsheet
https://www.qld.gov.au/education/schools/procedures/health
https://www.safework.nsw.gov.au/__data/assets/pdf_file/0006/586347/guide-to-machine-safety.pdf
https://www.australianworkplacesafety.com.au/safe-use-of-machinery-and-equipment-in-australian-workplaces/
https://education.qld.gov.au/curriculum/stages-of-schooling/CARA/activity-guidelines/practical-workshop-activities

## Slide 4: Metal Lathe tooling materials
TOOLING MATERIALS
Description: A tough, durable steel alloy that retains its hardness at higher temperatures.
Best For: General-purpose cutting, especially on softer metals like aluminium, mild steel, and brass.
Pros: Extremely hard and wear-resistant, Can be used at high speeds, Provides excellent surface finish
Cons: Brittle – can chip if dropped or used improperly, More expensive
Pros: Easy to sharpen, Inexpensive, Good for slower-speed lathes
Cons: Wears faster than harder materials
High-Speed Steel (HSS)
Carbide (Tungsten Carbide)
Description: A very hard, heat-resistant material made from a compound of carbon and a metal (usually tungsten).
Best For: High-speed cutting, harder metals (like stainless steel, cast iron, titanium).
Cobalt High-Speed Steel (HSS-Co)
Description: A version of HSS with added cobalt (usually 5–8%).
Best For: Tougher metals like stainless steel and tool steel.
Pros: Higher heat resistance than standard HSS, Stays sharp longer
Cons: Slightly more expensive than regular HSS

## Slide 5
TOOLING MATERIALS
Description: Made from aluminium oxide or silicon nitride.
Best For: High-speed finishing operations on hard materials (often used in production machining).
Pros: Combines hardness and toughness, Resistant to wear and heat
Cons: Still relatively brittle, expensive
Pros: Extremely high heat resistance, Very hard
Cons: Very brittle, Not suitable for interrupted cuts or roughing, expensive
Ceramics
Cermet (Ceramic + Metal)
Description: A hybrid of ceramic and metal materials.
Best For: Finishing cuts on steels, providing high-quality surface finishes.
Diamond (PCD – Polycrystalline Diamond)
Description: Industrial diamond particles fused together.
Best For: Non-ferrous materials (aluminium, copper, plastics, composites).
Pros: Ultimate wear resistance, Long tool life
Cons: Very expensive, Not suitable for steel or iron (causes chemical wear)

## Slide 6: Metal Lathe tooling materials
TOOLING MATERIALS
HSS Tooling | Carbide (Tungsten Carbide) | Cobalt High-Speed Steel (HSS-Co)
Ceramics | Cermet (Ceramic + Metal) | Diamond (PCD – Polycrystalline Diamond)

## Slide 7: Lathe tooling and their application
STYLES OF TOOLING
Operations on the lathe can consist of multiple movements. Most processes have there own tooling and generally consist of roughing and finishing passes. Below are some of the basic lathing operations and the style of tooling used.
O.D (outside diameter) Turning;
  Straight (plain) turning; Removes material along the entire length to bring a bar down to size.
  Taper turning; Produces a gradual change in diameter.
  Facing; Squares the end of a work piece.
  Spot facing; Creates a small flat seat for bolt heads or washers.
Roughing tool (tungsten insert)
Finishing tool (tungsten insert)
HSS OD turning tools

## Slide 8
STYLES OF TOOLING
Additional external cutting and forming tools;
  Chamfering;. Cuts a 45° (or specified) bevel on an edge.
  Single‑point thread cutting; Tool follows lead screw; use a thread dial on manual machines, or CNC cycle.
  Parting off; Separates finished part from bar stock.
  Grooving; Cuts recesses for O‑rings, snap rings, or design features..
  Knurling; Imprints/forms a pattern for grip or texture.
HSS Parting/grooving tool
Tungsten carbide parting/grooving tool
45 Chamfering tool
Single point threading tool
Knurling tool

## Slide 9
STYLES OF TOOLING
I.D (internal diameter) Turning;
  Boring; Enlarges and trues a drilled hole.
  Internal taper boring; Produces a tapered bore.
  Thread boring (internal threading); Cuts threads in a bore.
Style of HSS Boring bar
Tungsten carbide boring bar (Roughing tip)
Tungsten carbide boring bar (finishing tip)
Tungsten carbide boring bar (threading tip)

## Slide 10: Lathe tooling cutting Direction
CUTTING DIRECTIONS
When machining on a lathe, you can cut forward/right-handed (towards the chuck) or backwards/left-handed (away from the chuck) by engaging the feeds or turning the saddle handle. These require your cutting faces to be on the side that is being driven into the material. That is why we also have “right hand” or “left hand” tooling. Another directional type of tooling is natural tooling. This means the tool can be plunged straight into the job like a parting or grooving tool.
Right hand
Left hand

## Slide 11: Lathe tooling geometry
CUTTING GEOMETRY
The cutting faces and the angles on lathe tooling is very important to how the tooling works. If the angles are too shallow or steep it can greatly affect how the tool performs or even doesn’t cut at all.

## Slide 12: Lathe tooling geometry
CUTTING GEOMETRY

## Slide 13
TOOLING CUTTING AND SET UP

## Slide 14: Setting tools on center in a tool holder
SETTING TOOLS TO CENTER
When setting and installing turning tools on the lathe it is crucial to set them on the centre of the axis of the spindle/chuck. If the tool is incorrectly set it can cause;
  Bitting
  Chatter
  Rubbing
  Squealing
It can also affect your tooling or component by;
  Improper tool wear
  Poor surface finish
  Possibly pull the tool into the work piece
  Break the tip or cutting edge of the tool
The easiest way to set your tool to the correct height is to align the tip up the the centre point of the dead/live centre when it is in the tail stock. After taking your first facing cut you will see if the tool is on centre or needs adjusting.

## Slide 15: Tool posts on the compound slide
TOOL HOLDERS
There are two types of tool holders that can be on the tool post of the lathe;
  Quick Change Tool Post (QCTP); Holds interchangeable tool holders that can be quickly swapped in and out by the dove tail style locking system on the back and adjustable height screw to set the tool on centre.
  Standard Tool Post; Can hold up to 4 tools and changed by rotating the tool post around. Each tool must be set to the centre height by shimming under the body of the cutting tool lifting it up to the required centre height.

## Slide 16: Tool posts on the compound slide
TOOL HOLDERS
Quick Change Tool Post (QCTP)
Standard Tool Post
Adjustable height screw

## Slide 17: resources
Photos;
http://toolnotes.com/home/machining/lathes-101/lathe-tools-and-toolholders/
https://www.aliexpress.com/item/1005004215921386.html
Video;
https://www.youtube.com/watch?v=J63dZsw7Ia4