## Slide 1: Basic Operations Of A Manual Lathe
Module 5.6

## Slide 2: Learning Objectives
LEARNING OBJECTIVES
By the end of this module, students will be able to :
Identify what a manual lathe is and what is it used for
Select safety features of a lathe and how to work safely around a lathe
Identify main parts and accessories on a lathe
Safe mounting procedures of materials
Evaluate speeds and feeds for machining on a lathe
Understand how to operate safely and basic understanding of machining procedures
Proper clean up and pack up of machine after use

## Slide 3: What is a manual lathe, and why would you use it???
LATHE EXPLANATION
A manual lathe is a machine used to shape materials such as metal, wood, or plastic by rotating the work piece against a cutting tool. It’s operated by hand and gearing mechanisms engaged by the operator, giving them full control over cutting speeds, depths, and feeds. Manual lathes are commonly used for tasks that involve turning, facing, drilling, forming and threading. They are ideal for learning basic machining skills, making one-off parts, and performing maintenance or repair work. While not suited for high-volume or complex production, manual lathes are regarded to be cost-effective and valuable in workshops where precision and flexibility are needed.
Notes: https://www.safeworkaustralia.gov.au/sites/default/files/2023-08/whs-principles-factsheets_overview_august2023.pdf - Factsheet
https://www.qld.gov.au/education/schools/procedures/health
https://www.safework.nsw.gov.au/__data/assets/pdf_file/0006/586347/guide-to-machine-safety.pdf
https://www.australianworkplacesafety.com.au/safe-use-of-machinery-and-equipment-in-australian-workplaces/
https://education.qld.gov.au/curriculum/stages-of-schooling/CARA/activity-guidelines/practical-workshop-activities

## Slide 4: Safety features on a manual lathe
LATHE SAFETY
There are a few safety features on manual lathes. You should always locate them and understand how they work before operating the machine. The standard safety features found across most manual lathes are;
  Guards around the chuck and spindle
  Manual set hard stops for the saddle side control
  E-stop button
  Foot pedal braking system

## Slide 5: PPE while operating the lathe
LATHE SAFETY
PPE (personal protective equipment) is the first thing you should think of before operating the manual lathe. There are many risks and hazards while operating the machine including;
Flying debris, rotating objects, moving parts, pinch points, sharp objects/surfaces and hot surfaces.
Here is a list of the PPE required to be wearing while operating the manual lathe;
  Safety glasses
  Hard Toe safety shoes
  Hearing protection (if required)
  No loose-fitting clothes or long sleeves
  Tie up long hair
  No jewellery
  No Gloves while the machine is being operated (Only while cleaning)

## Slide 6: Safe working area around a lathe
LATHE SAFETY
Make sure the working area around and on the lathe is in a clean, tidy and safe state. It is important to reduce any hazards while operating a lathe. If there is left over swarf (metal shavings), coolant or oils left on the lathe, it can create a hazard while operating the machine, cutting your hands or having your hand slip when turning the handles.
The surrounding area should also be clear of objects or obstacles that can impede your movement around the machine or any exits that you may need to move down quickly.
Class activity!!!
Look at the photo to the right and try identify some of the hazards….

## Slide 7
SAFETY PHOTO

## Slide 8: Identifying the main parts of a manual lathe
IDENTIFYING PARTS
.
Head stock; Main body that holds all the gears and drives
Spindle; The main part the turns and drives the chuck
Chuck; Material mounting point
Tool post; Holds the tools used for machining
Compound rest; Moves the Tool Post and can be set at required angles
Cross Slide; Moves the tooling in the X-axis
Saddle; sits over the bed and holds all the moving parts
Tail stock; Holds attachments used on the lathe
Hand Wheels; a way to drive and move the machine
Guide ways; Keeps the saddle running true to the machine
Bed: A part of the frame that runs along the X-axis
Feed screws; Provides automatic feeds controlled by Gearing in the head stock
Leg; A part of the frame that holds up the machine
Apron; Holds the Hand wheels for the Z movement and the auto feed engagement levers
Carriage; Has the gearing that engages the Feed screws and the Z-axis gearing
Chip Pan; Catches and holds all the Swarf from machining
FEED SCREWS

## Slide 9: Accessories used on a manual lathe
MANUAL LATHE ACCESSORIES
Some accessories that can be used on the lathe to assist in the machine processes include;
Tailstock: Holds tools like drill chucks or centres for supporting long work. Is adaptable with Morse Tapers. Once locked can be extended in the Z axis by turning the hand wheel at the back.
Steady rest: Supports longer work pieces during turning sits on the guide ways and gets locked in position.
Traveling Steady: Attaches to the saddle and moves along with the tooling keeping the work piece steady
Some centres that can go in the tail stock

## Slide 10: Material mounting options
WORK PIECE MOUNTING
There are a few options for mounting the work piece to the lathe for machining. Typically, a machinist will mount the part in the jaws of a chuck, attached to the spindle. The two main types of chucks are;
Three Jaw chuck; This is the fastest way of mounting material on the lathe and having it running concentric with the spindle, as the three jaws move simultaneously (self centring). But only having three jaws it is best suited for holding round or hexagonal objects.
Four Jaw chuck; Has four independently moving jaws which make centering the work piece to the spindle more challenging but can be done with the aid of a dial indicator. Having four jaws makes this chuck more suitable for irregular shapes, rougher material and trying to re-machine a part. Another benefit of a four-jaw chuck, it allows for more grip to the material for more locking strength.
Dial indicator

## Slide 11: Safe work piece mounting procedures
SAFE MOUNTING PRACTICE
Once you have selected the chuck you are going to be using, make sure the machine is off before you attempt mounting the material. The jaws on all the chucks are opened and closed by a chuck key. NEVER leave the chuck key in the chuck. Best practise is to only have it near the machine while you're holding on to it (some keys will even have a spring to stop them being left in the chuck).
Place as much of your material is in the chuck jaws as possible to increase the surface area that the jaws can grip onto. Then tighten up the chuck ensuring it is making contact squarely and evenly across the material.
Once you are happy that the job is mounted securely in the chuck, put the drives of the spindle into neutral and spin the chuck by hand making sure it looks like the material is turning straight and concentric

## Slide 12: Using a Centre in your material/part
LIVE/DEAD CENTRE
If your job is hanging out to far, consider using a live/dead centre to help stabilize it during the machining process. To use the centres, you will need to centre drill the end of the work piece for a centre to engage in. The live centre has bearing in it that allows it to spin with the the job where the dead centre doesn’t spin and needs lubrication to work.
Centre drilling
Live centre
Part being held by live centre
Centre Drill

## Slide 13: Speeds and feeds for machining on a lathe
SPEEDS AND FEEDS
Knowing your spindle speeds and tooling feed rates are crucial for machining process. It is how you archive specific surface finishes required for each job. Using these calculations will get you cutting correctly but you may need slight adjustments with the variation of your material quality and what type of cutter you are using.
Starting with spindle speeds. Its very similar to drilling speeds we covered off on earlier, the difference is instead of using the diameter of the drill bit you calculate it off the diameter of the material you are cutting (so your spindle speed rate should change while machining)
For example;
“Simplified formula”
RPM = (Cutting Speed (m/min) * 300) / Material diameter (mm)
Cutting Speeds m/min;
Stainless steel = 12
Tool steel = 18
Cast iron = 24
Malleable iron = 27
Medium carbon steel = 30
Free cutting steel = 43
Aluminium/ Brass = 61
Wood/ Plastic = 91
“example”
RPM = 30 * 300 = 9,000 ÷ 12 = 750 RPM
Medium carbon steel
12mm material diameter
“example”
RPM = 12 * 300 = 3,600 ÷ 8 = 450 RPM
Stainless steel
8mm material diameter

## Slide 14: Spindle speed exercises!!
SPEEDS AND FEEDS
“exercise 1”
RPM = Cast Iron * 300 = ?? ÷ 4mm = RPM
Cutting Speeds m/min;
  Stainless steel = 12
  Tool steel = 18
  Cast iron = 24
  Malleable iron = 27
  Medium carbon steel = 30
  Free cutting steel = 43
  Aluminium/Brass = 61
  Wood/Plastic = 91
“exercise 2”
RPM = Aluminium * 300 = ?? ÷ 6mm = ?? RPM
“exercise 3”
RPM = Plastic * 300 = ?? ÷ 9mm = ?? RPM
Notes: Work through as a class

## Slide 15: Setting the spindle RPM on the Lathe
SPEEDS AND FEEDS
Setting the spindle speed on the lathe is done by moving levers on the front of the head stock into the corresponding position. Most lathes with have a “high” and “low” gear ratio with various speeds in each section by selecting the right gears. They can also have a “high”, “medium” and “low” Gear ratio with multiple speeds to select in each level ( tip: it sometimes helps to move the spindle by hand to get the gears to mesh, DO NOT ATTEMPT TO CHANGE SPEEDS WHILE THE MACHINE IS RUNNING).
Spindle speed location

## Slide 16: Tooling feed rates
Tooling feed rates refers to the speed at which the tool is being fed into the material.
The spindle speed, the material selection and tooling type, all affect the feed rate.
The Feed rate gets measured in mm/rev (millimetres per revolution)
SPEEDS AND FEEDS
For basic machining on a manual lathe, it is safe to follow this as a rule of thumb for mm/rev;
  Roughing passes: 0.2 - 0.5 mm/rev
  Finishing pass: 0.05 – 0.15 mm/rev
MM/

## Slide 17: Setting the feed rate on a manual lathe
To set the feed rates, locate the machines federate chart. Generally, the feed charts will be located on the head stock of the lathe. Once you locate the desired feed rate, there will be a series of letters and numbers next to it and you must engage the corresponding levers to the matching letters and numbers. As you can see below the lathe feed chart is all the way down the bottom of the chart below the thread cutting columns.
SPEEDS AND FEEDS
Levers to change the feed rate
Feed rate chart
Gears to change the feed rate

## Slide 18: Lathe movement axis
LATHE AXIS
Manual lathes run in two main axes, Z and X. A good way to remember if you are moving in the minus or positive directions, is if you are removing material then you are traveling in the minus direction.

## Slide 19: Manual lathe operation
MANOEUVRING THE LATHE
To position the tooling (move the saddle in the Z-axis and the cross slide in the X-axis) locate the hand wheels on the apron. The big main wheel down the bottom will move the whole saddle in the Z-axis, the smaller hand wheel above will move the cross slide in the X-axis. For the first time on the lathe, it is good practice moving the saddle and cross slide around when the lathe is switched off, in a safe position where you won’t crash. This is to allow yourself to get use to the directions of travel and how the lathe moves.
X-axis travel
(move the cross slide)
Z-axis travel
(move the saddle)

## Slide 20: Starting the spindle on the lathe
STARTING THE LATHE
After double checking the jaws of the chuck are tight on the work piece and the correct spindle speed has been selected, you can start up the lathe.
It is always good to “jog” the lathe before completely starting it, making sure the speed is correct and checking that none of the automatic feeds are engaged. There is normally a jog button on the lathe, if not you can slightly and carefully push down the leaver to make the spindle start, then pull back to the neutral position.
Always make sure the safety guards are in the correct position before starting the machine.
Lever to start the machine
Jog button

## Slide 21: Position referencing
To know how far the machine has travelled there are two main ways. The most common way is using a D.R.O (digital read out), which can tell you how far you have moved in the Z and X axis. With a D.R.O you can “Zero” your axis datums. Using a D.R.O it makes machining easier by displaying the movements live, making it less likely to have errors
The other way is to read the analogue dials on the hand wheels that control the Z and X axis, you can also “Zero” these dials by rotating them.
COORDINATE SYSTEMS
D.R.O
Analogue Dials

## Slide 22: Setting the datum points on a lathe
“Datum points” are the points on the material that you reference off. Normally the outer most parts of the stock material. This is where you will reference your drawings from and start the machine process.
To set your datum points bring the tool in close to the material to be machined. While the machine is running, turn the X-axis hand wheel slowly until your tool just touches the material and starts to shave away the material, then either “Zero” your D.R.O or your analogue dials.
Once you have done the X-axis, move the tooling to the front of the material and do the same in the Z-axis.
When the datums are set, you can begin machining the material.
DATUM POINTS
X-AXIS
Z-AXIS

## Slide 23: Engaging the auto feed
Before you machine the material, it good practise to move the tooling to a position on the bed where it if free from collision points and engage the auto feeding mechanism. Make sure it is traveling in the right direction and at the correct feed speed you set.
To engage the auto feed, there is a lever on the apron of the machine. Push down on the lever and the machines will start to traverse along the bed or cross slide in the direction you set it at. Before you reach your desired depth, disengage the auto feed and use the hand wheels to finish your depth. Continue this process remembering your roughing and finishing passes, until the part is finished.
SPEEDS AND FEEDS
Auto Feed lever

## Slide 24: Cleaning the machine
CLEANING
When you have finished using the manual lathe, apply best and safe practices to clean it down.
Make sure the machine is completely turned off before you start the cleaning process.
If you are handling sharp objects, make sure you wear the correct gloves.
Use a vacuum, pliers (if the swarf is stuck) and rags to clean down the lathe.
Remove tooling from the tool post and store away.
Once it is clean use some oil or oil-based spray to clean and wipe down the bed ways for longevity of the machine.

## Slide 25: resources
Photos;
https://www.goldenmachinery.com/blogs/5-main-parts-of-a-lathe-machine
https://en.wikipedia.org/wiki/Lathe
https://newsigns.com.au/products/no-gloves-in-toilet-sign
http://www.homews.co.uk/page548.html
https://www.istockphoto.com/search/2/image-film?phrase=people%20doing%20math%20equations
https://www.machineryhouse.com.au/l639d